## Slide 1
M19800 & M9800
Folding Door
Notes: Bi folding door system

## Slide 2
What
M19800 and M9800 are SMARTIA systems for folding doors, insulated and non-insulated, top-hung, for normal and heavier constructions and address to middle-end projects.
Both are inexpensive and effective solutions for the folding doors market.
M19800 & M9800 Bi-Folding

## Slide 3
Why
to divide and isolate spaces both internally and externally
to provide our proposal for folding doors of high performance and standards equal to the other SMARTIA systems
to offer an extensive range of sturdy and versatile solutions (offices, hotels, café, “winter-garden”, always at a reasonable price
M19800 & M9800 Bi-Folding

## Slide 4
Vent or Frame width: 50 mm
Vent height: 65mm
Frame height: 30mm
Vent weight: up to 100 Kg
In-floor sill height: 4.5mm
Glazing: 24 to 32mm
Insulation Uw: 2,8Wm2/K
Max heights: 3.0 - 3,5m
M19800 & M9800 Bi-Folding
Notes: Frame sash condition

## Slide 5
Frame/ Vent width: 100mm (M9800)
107mm (M19800)
Adjustable Frame/ Vent width: 117mm (M9800)
126mm (M19800)
Vent/ Vent height: 130mm (M9800)
142mm (M19800)
M19800 & M9800
Sight line
Notes: Frame sash condition

## Slide 6
n+ 0
n + 1
n + m
(odd numbers)
Outwards and inwards opening of vents and door
With glass panel and blinds
M19800 & M9800
Typologies

## Slide 7
Frame: top-guide, bottom guide and side profiles, and 90o cutting and no cleat corners
Vent: 1 single profile and 45o cutting
Μ19800 & Μ9800
Cuttings

## Slide 8
M9800 Thresholds
4 different threshold profiles
Normal top-mounted with insulating wing
Low top-mounted with insulating wing (different bottom roller)
In-floor (concealed)
Low on-floor placement (flexible)
New flat with new roller (concept)

## Slide 9
M19800 Thresholds
2 different threshold profiles
Top-mounted with insulating wing
In-floor

## Slide 10
Top-hung bi-folding door
Special heavy-duty roller hinge for top-hung (125Kg per vent, 250 Kg per roller)
2 special roller hinges at bottom threshold for vents alignment
  one of the normal guide and
  one for the low guide
M19800 & M9800 Roller Hinges
Notes: Roller of 35mm
Alligner of 33 mm, to prevent the relocation of the sash

## Slide 11
Structure adjustment for easier installation
Vertical adjustment of 20+20mm with double-frame profile
Horizontal adjustment of 20mm with double-frame profile
M19800 & M9800 Adjustment
Notes: regulators

## Slide 12
Double EPDM gasket
Possibility of perimetrical gasket placement for top insulation
Alternatively, with weathering brushes on the vertical
M19800 & M9800
Gaskets

## Slide 13
Intermediate vents locking
  with normal handle and getriebe
  with flush handle (albatros)
  With latch (1st vent)
Entrance door with various locking possibilities and Alumil brand handle
CF85 Bi-Folding
Locking

## Slide 14
M19800 & M9800 T support
Extra vent support for the vent frame with horizontal placed T profiles

## Slide 15
Wide variety of solution with various thresholds, typologies, thermal and non-thermal version
Minimal design with less aluminium (sufficient sight line)
Easy fabrication / installation
Achieve high dimensions (3.0 to 3.5m) and may cover wide openings (many vents)
M19800 & M9800 BENEFITS

## Slide 16
High performance in terms of thermal insulation, air and water sealing (4-sided EPDM, thresholds, etc)
Inexpensive solution with relatively light profiles
Flawless functionality
Anti-burglar Security
M19800 & M9800 BENEFITS

## Slide 17
THANK YOU
FOR YOUR ATTENTION