## Slide 2
What
Thermally insulated sliding system
Minimal aesthetics similar to S650 PHOS
Competitive price similar to S560

## Slide 3
Why
An economical solution for minimal thermally insulated windows
Gain market share from competitors with similar systems in LSP and residential market
SMARTIA system available to all fabricators so as to penetrate the market efficiently

## Slide 4
Benefits

## Slide 5
6
Maximum visibility & sense of freedom
5
Minimal design with concealed frame
3
Easy & safe access with flat frame flush to the floor
2
Energy & cost saving thanks to the high thermal insulation
4
High security with multi-locking mechanism
1
Total comfort thanks to the high sound reduction level
Benefits

## Slide 6
Sound reduction 42dB
Certified performance from the Aristotle University of Thessaloniki
IGU 32mm
Minimal installation with concealed frames
Benefits
Total comfort
Notes: IGU = Insulated Glass Unit

## Slide 7
Thermal insulated profiles
Fiberglass reinforced polyamides 24 & 20 mm width
PVC profiles at the bottom frame & at the interlocking profile
IGU 32 mm
Benefits
Energy & cost saving
Notes: IGU = Insulated Glass Unit

## Slide 8
Easy & safe access
Easy access with total flat frame
Ideal for children, elders & people with disabilities
On-floor installation with only 32mm frame height
Ideal for renovations
Benefits
32mm

## Slide 9
High security
Multi-locking mechanism with 5-year guarantee from ALUMIL
Difficulty to push up the sash with the extra anti-lift accessories of the mechanism for maximum security
Benefits

## Slide 10
Benefits
PHOS series with less visible aluminium surfaces
Maximizing glass pane
Concealed sash into the frame
Concealed frame into the ceiling and the walls
Minimal design
95mm
63mm
74mm

## Slide 11
74 mm
Minimal version
Frame is concealed all around with plasterboard
Standard version
Frame is visible all around with 74mm aluminium width
Frame flush to the wall
Benefits
Maximum natural light and sense of freedom

## Slide 12
Narrow interlocking profile with 44mm visible face width
Benefits
44mm
Maximum natural light and sense of freedom

## Slide 13
Attention to detail

## Slide 14
Technical characteristics
Attention to detail
155mm
32mm
Visible frame-sash height 63/94mm
Frame height 32 mm
Frame width 155 mm
Sash width 63 mm
Interlocking profile width 44 mm
Sash weight up to 250 Kg
Glazing width 32 mm
Thermal insulation Polyamides, PVC
63mm
94mm

## Slide 15
Available typologies
Attention to detail
Double track
Triple track
Meeting stile
Flyscreen
Pocket typology
Corner typology

## Slide 16
Use of glazing bead for easy glazing installation and sash fabrication
Glazing thickness up to 32mm maximum
Attention to detail
Glazing

## Slide 17
Attention to detail
Static loads

## Slide 18
Attention to detail
Static loads

## Slide 19
Attention to detail
Static loads

## Slide 20
International patented locking mechanism
Minimal aluminium handle designed & developed by ALUMIL
Attention to detail
Locking mechanism

## Slide 21
Available in powder coating (black, white & silver)
Easy installation on site
Easy replacement
Attention to detail
Locking mechanism

## Slide 22
Alternative design with the handle having same height with the total height of the sash
Place the standard handle
Above and below the handle, place the glazing bead M63177 that has the same geometry with the internal handle
Creates the continuity of the handle and offers advanced aesthetics
Attention to detail
Locking mechanism

## Slide 23
Attention to detail
Locking mechanism
With M63177
Without M63177

## Slide 24
Multi-point lock
Wide range of locks from 300 mm sash height (developed by GU specific for ALUMIL)
From 1 up to 4 locking points
Anti-lift striker for enhanced security
Attention to detail
Locking mechanism

## Slide 25
Maximum weight per sash up to 250 Kg
Stainless steel rollers
Use of heavy duty inox rail or U-type inox rail with reinforcement
Attention to detail
Gliding

## Slide 26
At the bottom of the sash brushes placed at both right & left edge caps protect the rollers from dirt & dust
Attention to detail
Gliding

## Slide 27
Functionality & credibility

## Slide 28
Set of central seals for the intermediate & the external part of the bottom frame
Functionality & Credibility
Central sealing

## Slide 29
Functionality & Credibility
Central sealing
Sash spacers are installed into the frame
Alignment of the sash
Sash anti-lift

## Slide 30
At the upper side of the frame the brushes of the cap of the interlocking profile seal with the spacer
Functionality & Credibility
Central sealing

## Slide 31
The low frame 32mm is certified up to 9 Bf (strong gale)
Wind speed 79,6 Km/h
Watertightness 300 Pa (class 7A)
Functionality & Credibility
Water evacuation
0
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 32
Special barriers placed at the chambers of the low bottom frame
For double and triple frame
Functionality & Credibility
Water evacuation

## Slide 33
Subsill profile for vertical water drainage
Alternative option for easier fabrication
Functionality & Credibility
Water evacuation

## Slide 34
Functionality & Credibility
Water evacuation
External grid with Subsill profile for vertical water drainage
Alternative option for easier fabrication

## Slide 35
Functionality & Credibility
Water evacuation
External grid with Subsill profile for vertical water drainage
Available drainage adaptor D25/D32
Facilitates water drainage through the subsills of SMARTIA M630 and SMARTIA S560LT series

## Slide 36
Functionality & Credibility
Fabrication
45o connection of the frame with crimp or mechanical corners
90o connection of the frame with the low threshold with plastic cap connectors
45o connection of the sash with crimp corners

## Slide 37
Set milling tool with spacer
Spacer is inserted into the profile to hold it straight while cutting with the milling tool
Functionality & Credibility
Fabrication

## Slide 38
Punching machine for the mechanical corners treatment
Existing punching machines can be used
Functionality & Credibility
Fabrication

## Slide 39
Functionality & Credibility
Fabrication
Special jig for the handle machinings
Reduces alignment faults of the internal & external handle

## Slide 40
Functionality & Credibility
Thermal Insulation
 | Ug = 1,3 | Ug = 1,1 | Ug = 1,0 | Ug = 0,8
Uw | 1,69 | 1,52 | 1,43 | 1,26
For a 2-sash typology 3,00m x 2,20m (W x H) and psi = 0,035 |  |  |  | 

## Slide 41
Certifications
Functionality & Credibility

## Slide 42
Commercial session

## Slide 43
SMARTIA
SUPREME
M630 vs ALUMIL series

## Slide 44
Technical characteristics | SMARTIA S560 sliding | SMARTIA M630 | SUPREME S650 low threshold
Visible alu face width | 108,5mm | 63mm | 42,5mm
Frame height | 31mm | 32mm | 35mm
Frame width | 136mm | 155mm | 164mm
Sash width | 56mm | 63mm | 62mm
Interlocking width | 49/86mm | 44mm | 25mm
Sash weight (max) | 180Kg | 250Kg | 1000Kg
Glazing | Up to 45mm | Up to 32mm | 46mm
Thermal insulation | 24 & 16mm polyamides, PVC | 24 & 20mm polyamides, PVC | 22 & 18mm polyamides, PVC
M630 vs ALUMIL series

## Slide 45
Performance | SMARTIA S560 sliding | SMARTIA M630 | SUPREME S650 low threshold
Air permeability | 4 | 4 | 3
Watertightness | 7A (300Pa) | 7A (300Pa) | 7A (300Pa)
Resistance to windload | C2 | C5 | C3
Sound reduction | 38dB* | 42dB | 41dB**
Burglar resistance | RC2* | - | RC2**
Thermal insulation Uw*** | 1,67 | 1,43 | 1,50
M630 vs ALUMIL series
* Performance for S560 L&S with standard frame
** Performance for S650 with concealed frame (in-floor installation)
*** For a 2-sash typology 3,00m x 2,20m (W x H) with Ug = 1,0 W/m2K and psi = 0,035

## Slide 46
Fabricators
Benefits
per personas
Differentiating in the market through minimal systems, following the modern architectural trends and with higher margins
Easy installation & maintenance
Fixed cost of sales due to sales per meter €/m
Product that meets a wide range of needs thanks to the variety of solutions
Increased clientele with minimal products ideal for hotel solutions & LSP

## Slide 47
Architects
Benefits
per personas
Minimal design with extensive glazing surfaces for ‘transparent’ architecture
Differentiating in the market through brand new innovative solutions
Product that meets a wide range of needs thanks to the variety of solutions with modern, minimal design and the structures for people with special needs
Designing “green” buildings with energy / money saving systems
Satisfying their clients and increasing their credibility

## Slide 48
Home owners
Benefits
per personas
Elegant coziness full of natural light thanks to the system's minimal design and the wide glazing surfaces
Cost & energy saving due to the great overall performance
Ease of use and long-lasting flawless functionality
Product that meets a wide range of needs thanks to the variety of solutions and the structures for people with special needs

## Slide 49
Technical catalog
Fabrication manual
Catalogs

## Slide 50
Promotional material
Pre-qualification brochure
Technical data sheet

## Slide 51
Thank you
for your attention