## Slide 2
Thermally insulated sliding system
Modern flat design with minimum visible sightlines
Ease & flexibility of construction
Of the highest performance for its category
What

## Slide 3
Why
A value for money solution for sliding thermally insulated windows & doors
Follows the architectural trends for less visible aluminium frames
Gain market share from competitors with similar systems in LSP and residential market

## Slide 4
Benefits

## Slide 5
4
Higher sound reduction with glazing up to 28mm
5
High security with multi-locking mechanisms
1
Maximum visibility with only 25mm sightline
2
Easy access with low threshold
3
Energy & cost saving thanks to the thermally insulated profiles

## Slide 6
Benefits
Maximum visibility
38mm
116 mm
38 mm
107 mm
85 mm
76 mm
Sash S350
Sash S350 LT

## Slide 7
Standard interlocking profile
Benefits
88,5mm
Maximum visibility
79,5mm
S350
S350 LT

## Slide 8
Narrow interlocking profile
Benefits
50,5mm
25mm
Maximum visibility
S350
S350 LT

## Slide 9
162mm
Adjoining profile
102mm
Benefits
Maximum visibility
S350
S350 / S350 LT

## Slide 10
Easy & safe access
Standard frame 38mm
Alternative use of low frame 32mm ideal for renovations
The only change is the height of the chambers
All sashes are applicable with both frames
Benefits
S350
S350 LT

## Slide 11
Available typologies
Benefits

## Slide 12
Pocket typologies
Sash slides into the wall cavity
Ideally combined with sliding flyscreen & shutter
Benefits

## Slide 13
Pocket typologies
Updated pocket cover profile that creates a hook with the pvc profile
  Improved sealing with 2 rows of gaskets and brushes
  Improved thermal insulation between wall and sash
  Improved aesthetics between wall and sash
Benefits

## Slide 14
Flyscreen
Two types of flyscreens:
Heavy duty S490
Light M868
Benefits
PVC accessory to hold the insect screen fabric for:
High aesthetics
Improved fabric stretch
Available in 3m bars

## Slide 15
Flyscreen
Narrow flyscreen for S350 LT with narrow interlocking 25mm
Benefits

## Slide 16
Rolling shutter
Ideally combined with rolling shutter system M13800
Unified thermal insulating zone
Special design for pocket sliding typologies to easily visit & repair the rolling shutter
Benefits

## Slide 17
Certifications
Benefits

## Slide 18
Thermal Insulation
 | Ug = 1,3 | Ug = 1,1 | Ug = 1,0
Uw | 1,89 | 1,73 | 1,66
For a 2-sash typology 3,00m x 2,20m (W x H) and psi = 0,036 |  |  | 
Benefits

## Slide 19
Attention to detail

## Slide 20
Energy & cost saving
1
1
2
1
Thermal insulated profiles
Fiberglass reinforced polyamides 24 & 22 mm width
PVC profiles perimetrically of the frame (same for standard and low frame)
116mm
Sash profile S384
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 21
Energy & cost saving
3
3
Thermal insulated profiles
3. Alternative use of sash with anti-distorsion fiberglass reinforced polyamides 24 mm width ideal for dark frames (reduces banana effect due to high temperature differences)
116mm
Sash profile S390
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 22
Energy & cost saving
4
4
107mm
Thermal insulated profiles
4. Alternative use of smaller sash with fiberglass reinforced polyamides 30 & 22 mm width
Sash profile S35013
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 23
Energy & cost saving
4
4
107mm
Thermal insulated profiles
Alternative use of smaller sash - compatible with narrow interlocking profile 25mm - with fiberglass reinforced polyamides 30 & 22 mm width
Sash profile S35011
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 24
Thermal insulated profiles
PVC profiles at the interlocking profile
Compatible with sash profiles S384, S390
Energy & cost saving
5
88,5mm
5
Interlocking profile
S384, S390
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 25
Thermal insulated profiles
PVC profiles at the interlocking profile
Compatible with sash profiles S35011, S35013
Energy & cost saving
5
Interlocking profile
S35011, S35013
Attention to detail
5
79,5mm
Notes: IGU = Insulated Glass Unit

## Slide 26
Thermal insulated profiles
PVC profiles at the narrow interlocking profile
Compatible with sash profiles S384, S390
Energy & cost saving
50,5mm
5
5
Interlocking profile S356
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 27
Thermal insulated profiles
6. PVC profiles at the narrow interlocking profile
Available as an accessory & easily placed by the fabricator
Compatible with sash profile S35011
Energy & cost saving
25mm
6
6
Interlocking profile S35017, S35027
Attention to detail
Notes: IGU = Insulated Glass Unit

## Slide 28
2 types of double glazing with the use of:
Wedges up to 26mm glazing thickness
‘U shape’ gasket up to 28mm glazing thickness
Analytical glazing list available at the system’s technical catalog
Glazing
18-26mm
28mm
Attention to detail

## Slide 29
Double rollers with maximum weight up to 180 Kg per sash
Αdjustable rollers for easier installation & maintenance
U-type stainless steel rail
Attention to detail
Gliding

## Slide 30
Use of special spacers fixed at the bottom of the sash
Available for all sash profiles
Attention to detail
Fixed lights

## Slide 31
Functionality & credibility

## Slide 32
Multi-point lock
Wide range of locks from 300 mm sash height (developed specific for ALUMIL)
Locking mechanism
Functionality & credibility

## Slide 33
Multi-point lock with hooks
Available only for standard sash 85mm
Locking mechanism
Functionality & credibility

## Slide 34
Sash assembly
Sash 45o connection perimetrically
Compatible with all sash profiles
Standard interlocking profile
Narrow interlocking profile 50,5mm
Sash 45o connection
Interlocking profile 45o/90o connection
Compatible only with sash profiles S384 & S390
1
2
Functionality & credibility

## Slide 35
Narrow interlocking profile 25mm
Sash 45o connection
Interlocking profile 90o connection
Compatible only with sash profile S35011
Standard or Narrow interlocking 25mm with 28mm glazing
Sash 90o connection
Interlocking profile 90o connection
Compatible only with sash profile S35011
3
4
Functionality & credibility
Sash assembly

## Slide 36
Sash 45o connection with mechanical corners
Punching machine for mechanical corners treatment
Functionality & credibility
Sash assembly

## Slide 37
Standard frame 45o connection with mechanical corners
Punching machine for mechanical corners treatment
Functionality & credibility
Frame assembly

## Slide 38
Frame assembly
Low frame 45o connection with force fitting corners
New patented corner design by Alumil
No treatment needed
Functionality & credibility

## Slide 39
Standard frame
The water follows its way out through the chamber of the frame
Punching machine for frame’s weep holes treatment
Water evacuation
Functionality & credibility

## Slide 40
Low frame
The water follows its way out through the rail wing
Existing punching machine can be used for frame’s weep holes treatment
Water evacuation
Functionality & credibility

## Slide 41
Set of elastic central seals for the upper & bottom frame
Same accessories used for the standard and low frame
Central sealing
Functionality & credibility
Standard interlocking profile
Narrow interlocking profile 25mm

## Slide 42
Special design of end caps when the same sash is used perimetrically
No treatment needed for the cover of the interlocking profile
Straight cut of the cover profile
Easier and faster fabrication
Interlock assembly
Functionality & credibility

## Slide 43
Special design of end caps when the narrow interlocking profile 25mm is used
The caps are also connectors between the interlocking profile & the horizontal sash
No treatment needed for the horizontal sash
Functionality & credibility
Interlock assembly

## Slide 44
Milling tool available
Same tool with an add-on accessory for the reinforced interlocking profile
Functionality & credibility
Interlock assembly

## Slide 45
Machinings's guide
Functionality & credibility
 | S350 | S350 LT
Sash’s Corner machining | Yes | Yes
Frame’s Corner machining | Yes | No
Standard interlocking Profile’s machining | No | No
Narrow interlocking Profile’s machining | No | Yes

## Slide 46
Comparisons

## Slide 47
Comparisons
S384
1,637Kg/m
S35013
1,268Kg/m
S35011
1,348Kg/m
-17,6%
-22,5%
Sash

## Slide 48
S352
1,610Kg/m
S35352
1,363Kg/m
-15,3%
Comparisons
Frame

## Slide 49
Maximum dimensions
Comparisons

## Slide 50
Maximum dimensions
Comparisons

## Slide 51
Maximum dimensions
Ix=6,4
Comparisons

## Slide 52
Maximum dimensions
Ix=41,1
Ix=75,8
Comparisons

## Slide 53
Commercial session

## Slide 54
Standard frame
Standard sash
Narrow interlocking profile 50mm
Low frame
Low sash
Narrow interlocking profile 25mm
Technical catalogs

## Slide 55
Benefits
per personas
 | Fabricators | Architects | Home owners
Modern design |  |  | 
Wide range of solutions |  |  | 
Increased clientele |  |  | 
Differentiation |  |  | 
Green buildings design |  |  | 
Cost & energy saving |  |  | 
Ease of use |  |  | 
Long-lasting functionality |  |  | 
Coziness |  |  | 
Easy fabrication |  |  | 

## Slide 56
The new solutions of SMARTIA S350 - S350 LT - offer:
Advanced modern aesthetics
Same thermal & sealing performance with older version
Easy and fast fabrication
Less cost with common accessories
Ideal solution for large scale projects
Ideal solution for renovations with low frame
Summarize

## Slide 57
Thank you
for your attention