## Slide 2
Supreme SF85 is ALUMIL’s proposal for a world-class folding door,
highly-insulated and bottom-slide,
with minimal aesthetics and outstanding performance,
for very large dimensions and extremely low sight-lines
In addition to SMARTIA MF65
Notes: Με άλλη εικόνα

## Slide 3
SUPREME SF85 was designed to offer competitive solutions for
high-end projects (extreme performance and large dimensions)
residential use (minimal design, long-lasting flawless use)
and strengthen the brand of ALUMIL by creating a unique product in the segment of high-end folding doors
Notes: Με άλλη εικόνα

## Slide 4
Technical Session

## Slide 5: Emphasis to detail
Sash depth: 85 mm
Operation bottom slide
Insulated highly
Glazing: 20-53mm standard 34-75mm structural
Max weight: 200 Kg/vent
Max height 4.0 m
Vent width up to 1.5 m
Technical Characteristics

## Slide 6
Flexibility of construction
Typologies*
Odd numbers
  n+0 e.g. 3+0
  n+1 e.g. 3+1
  n+m e.g. 5+7
Semi-structural sash version
Corner construction
Inward / outward opening
Even numbers
  m+0 e.g 4+0
  m+1 e.g 2+1
  m+n e.g 2+3
  m+m e.g 2+2
Notes: Εικονίδια για τυπολογίες

## Slide 7
Standard structure
Corner structure
Corner structure
Notes: Εικονίδια για τυπολογίες

## Slide 8: Emphasis to detail
Special bottom roller-hinge
  Max weight 500Kg (compet. 200Kg)
  Anodised body, stainless steel rollers and rust-protected bearings
  Allows very large dimensions (height, panel width and overall width)
  Enables very easy installation and long-lasting flawless operation
  Anti-lift protection for burglar protection
Features & Fittings

## Slide 9: Emphasis to detail
Special top roller-hinge
Apart from just guiding the vents,
  it takes some of the weight “helping out” the bottom one (special spring system)
  it is quite longer than usual to prevent vents from turning while operation
Features & Fittings

## Slide 10: Emphasis to detail
Heavy-duty hinges, with 3 sets being adequate for normal structures, i.e. 2.6m high. Available in silver and black anodising
Pull-handle attached on the hinge to easily move the vents together
Flat handle for the intermediate vents, with Alumil logo and option to be locked
Standard handle with spindle for the door, with Alumil logo and design
Features & Fittings
3
2
1
3

## Slide 11: Emphasis to detail
Double guide rail, made of inox, solid or hollow
Adjustable frame easily set with special fittings (5mm left & 5mm right)
Rubber fitting placed around the roller-hinge to allow simple cut of the sash gasket
Special cap to cover the milled part of the track (for inserting the vents)
Gasket to cover the track beneath the door
Features & Fittings
Emphasis to detail
3
2
1
4
4

## Slide 12: Emphasis to detail
Quadruple (not double) locking latches made of glass reinforced polyamide or aluminium (RC2)
Single gasket from co-extruded EPDM and foam
Double polyamides 40mm and “Alumil energy bar”
PE insulation foam (under the vent, around the glass, etc)
Lock extensions (>2550, 2750, 3050mm
Features & Fittings
3
2
1
4

## Slide 13: Emphasis to detail
Sealing gasket at the bottom for enhanced tightness, and possibility for brush
Special foam bar at the bottom part of the sash apart from the NRG bars infills
Hollow glazing beads for enhanced security
Features & Fittings
2
1
3

## Slide 14: Emphasis to detail
Features & Fittings
Three (3) sash options
Standard sash
Straight lines sash
Semi-structural sash

## Slide 15: Emphasis to detail
Three (3) threshold options
Standard threshold
Low threshold
Embedded, concealed threshold
Sub-sill add-on for extra watertightness
Features & Fittings
2
1
3

## Slide 16: Emphasis to detail
Door holdback magnet
Adequate space for applying ventilation trickle
Easy plaster application (due to the frame wing)
Generally, thin less-noticed glazing gaskets (aesthetical)
Glazing setting blocks (instructions)
Features & Fittings
2
3
4
5
top rail
sash profile
frame profiles

## Slide 17: Emphasis to detail
Corner construction for commercial and residential use
Compatible with all solutions (inward/outward, normal/low threshold, semi-structural sash)
Features & Fittings

## Slide 18: Basic sections
Sash & top rail
Horizontal section with adjustable frame profiles and sash ones
Sash & bottom rail (threshold)

## Slide 19: Basic sections
Sash & door panel meeting point
Door closing point at a corner structure

## Slide 20
Air permeability EN12207:2016-12
CLASS 4
Watertightness EN 12208:1999-11
Resistance to windload EN 12210:2016-03
Thermal insulation EN 10077-2
CLASS 7A / 9A (subsill)
CLASS C3/B3
Uf from 1.5 W/m2K
Remarkable performance certified by German Institute IFT ROSENHEIM
Certifications
Burglar resistance EN 1627-1630
RC2 (and PAS24 UK)
Uw= 1.00 W/m2K (2.6x3.0m with 3 vents and Ug=0.6 W/m2K
Uw= 1.16 W/m2K (2.6x3.0m with 3 vents and Ug=0.8 W/m2K
Uw= 1.03 W/m2K (3.45x3.0m with 3+1 vents and Ug=0.6 W/m2K
Uw= 1.18 W/m2K (3.45x3.0m with 3+1 vents and Ug=0.8 W/m2K

## Slide 21
Maximum Panel Dimension for given Wind pressure
with steel stiffeners
with out steel stiffeners
semi-structural sash
E.g. 800Pa with steel stiffeners
Vent width 1.2m and height 3.6m

## Slide 22
Folding door operation
Inwards
Outwards
Door
first to open, last to close
Notes: new

## Slide 23
Fabrication details
The technical catalogue serves as a fabrication manual, presenting a wide set of machining instructions
CNC is required
Special Jig tool for hinges installation
Adjustable frame profiles come predrilled
Notes: new

## Slide 24
Commercial Training

## Slide 25: Unparalleled benefits
  height up to 4.0m, (competition stays at 3.0m)
  total width almost “infinite”
  vent width up to 1.5m (competition stays at 1.2m)
Ideal for modern residences, esp. when fewer panels are requested (5 panels of 1.4m instead 7 panels of 1.0m)
Unique for projects with 4.0m high structures and many vents
1. Extremely Large Dimensions

## Slide 26: Unparalleled benefits
MINIMAL DESIGN with much less aluminium and amazingly reduced sight lines. Elegance without compromise.
    vent/vent 105mm (competition usually at 120-125mm)
    frame/vent 110mm
    vent width 1.5m
    which reduces the number of the necessary panels, e.g. five instead of seven.
2. Incomparable Aesthetics

## Slide 27: Unparalleled benefits
WIDE VARIETY of solutions
All odd & even numbers of vents, i.e. 3+0, 4+1 and 2+3
Corner construction
Semi-structural version (vents)
In and outwards opening
3. Complete Range of Solutions

## Slide 28: Unparalleled benefits
EXTREME PERFORMANCE as with all ALUMIL SUPREME series
  air permeability, class 4
  wind load resistance, class C3/B3
  water tightness, class 9A
IFT Rosenheim certified
thanks to co-extruded special central gaskets, NRG, quadruple locking latches, profile sturdiness, etc.
4. Extreme Performance

## Slide 29: Unparalleled benefits
Market-leading THERMAL EFFICIENCY and excellent overall U-values
Uf from 1.5 W/m2K
2.6x3.0m with 3 vents Ug=0.6 W/m2K
Uw= 1.0 W/m2K with Ug=0.6 W/m2K
Uw= 1.16 W/m2K with Ug=0.8 W/m2K
Uw= 1.39 W/m2K with Ug=1.1 W/m2K
5. Energy Saving
co-extruded foam EPDM central gasket, kooltherm core, double 40mm polyamides, PE insulation foam

## Slide 30: Unparalleled benefits
Top levels of SECURITY and burglar protection, meeting all industry security standards.
  quadruple locking latches from glass reinforced polyamide (instead double)
  Bottom roller-hinge with anti-lift mechanism, profile and hinges sturdiness, 5-point lock, extensions, thick glazing
  “PAS24:2016” and RC2 certification
6. Burglar Resistance &
Safety Feeling
VIDEO RC2
Speaking of safety, there’s no risk of injuring fingers when operating (sufficient space)

## Slide 31: Unparalleled benefits
Smooth OPERATION and long-lasting flawless FUNCTIONALITY
Special roller hinges, both bottom and top
Heavy-duty hinges
A 5+1 structure (6 vents) which may weigh more than 1tn, is operated just with two sets of roller-hinges
7. Flawless & Long-lasting Operation

## Slide 32: Unparalleled benefits
Easy FABRICATION and trouble-free INSTALLATION
roller-hinges can hold the unhinged vents
single gasket instead of pair
frame adjustment -6 & +10mm
easy plaster application
easily applied vent trickle
8. Fabrication & Installation Ease

## Slide 33: Unparalleled benefits
Coating & Anodising by ALUMIL
Rust free fittings
Great variety of colors
Unparalleled quality
Possibility for pre-anodizing for maximum corrosion protection
Possibility for bi-color profiles (in/out side) for multiple aesthetic needs
9. Surface treatment

## Slide 34
Benefits for
ARCHITECTS
A very helpful architectural tool, which offers freedom of design, thanks to the great variety of solutions (vent number combinations, corner, semi-str, oversizing)
The series meets the standards required in high-end projects and provides the architect with a competitive advantage against other bidders
Allow the designing of buildings with energy / money saving systems
Help them differentiate from the market with a world-class product, thus upgrading of his/her status with such innovative solutions
Have their clients satisfied and architects credibility guaranteed

## Slide 35
Benefits for
FABRICATORS
Manufacturing: easy & time-saving, with simple cuttings and millings, without any punching machines required
Installation: easy and without risk of damaging the structure due to the special set of roller-hinges
Fixed cost of profiles due to sales per meter €/m
Higher margins since the product meets the specs of the demanding high-end projects
Product that responds to a wide range of needs thanks to the variety of solutions
Increased clientele with minimal products ideal for hotel solutions & LSP

## Slide 36
Benefits for
OWNERS
Elegant coziness full of natural light thanks to the limited sight lines and the fewer vents needed
Money & energy saving due to the great overall performance
Smooth operation and long-lasting flawless functionality
Product that responds to a wide range of needs (m+n, corner, semi-str.) and the structures for people with disabilities (low threshold)
Increased security feeling thanks to the high levels of burglar resistance (RC2, PAS24)

## Slide 39
THANK YOU
FOR YOUR ATTENTION