## Slide 2
What
SMARTIA MF65 and SMARTIA MF6500 are the bottom-slide, insulated & non-insulated folding door systems with minimal aesthetics & of very high performance.

## Slide 3
Why
Upgrade our folding door product-range & meet SMARTIA segment specifications
Change to bottom-slide operation and incorporate state-of-the-art accessories
Follow architectural trends for minimal design and low face-width
Present a competitive solution in terms of technical features, performance & cost
Meet every need for use in residential and commercial premises

## Slide 4
Technical section

## Slide 5
3
Sash to sash sightline 88mm
4
Same frame perimetrically (45° cut)
5
Glazing width 24-44mm (double & triple)
6
Frame to sash sightline
100mm
2
Sash thickness
65mm
Technical Characteristics
Bottom-slide operation
1
7
Max weight: 140 Kg/vent
Max dimensions, e.g. 1.0x2.8m

## Slide 6
Inwards / outwards opening
Odd / even numbers
  n+0 e.g. 3+0, 2+0
  n+1 e.g. 3+1, 2+1
  n+m e.g. 7+3, 4+4
Corner construction
Typologies

## Slide 7
2
Robust hinges
1
Special roller-hinges (odd)
4 rollers
up to 140 Kg per vent
(95 per bearing/roller)
adjustable at installation
rust-free / anti-lift
3
Solid inox rails
Accessories
4
Foam insulating materials

## Slide 8
Accessories
2
Various caps
Special roller-hinges (even)
2 rollers
up to 140 Kg per vent
EPDM gaskets
3
4
Special gasket fitting integrated with roller-hinge
1

## Slide 9
1
2
3
Pull handle
NRG bars, foam fittings, up to 32mm polyamides
Aluminium design flat handle
Accessories

## Slide 10
2
Adjuster for quadruple bolts
1
Quadruple (or double) shoot bolts (polyamide or alum.)
Accessories
3
Crimp or mechanical cleat corners (sash & frame)

## Slide 11
Frame profile
Same frame/rail profile perimetrically !!!
45° cutting (sash, frame)
Horizontal adjustment (-2 +5 mm), only with screws
Basic Sections

## Slide 12
Sash profiles
Basic Sections
Basic insulated sash
Bottom ΜF65 sash (alternative)
Basic non-insulated sash

## Slide 13
Low threshold
Standard insulated threshold
Basic Sections
With subsill
Standard non-insulated threshold

## Slide 14
Basic Sections
3+0
3+1 Door 3+3 meeting style
additional wing profile for adjoining, which needs a simple cutting

## Slide 15
Basic Sections
2+0
2+1 Door 2+3 meeting stile

## Slide 16
Basic Sections
Even Typologies
Special gaskets for air-tight sealing in the middle
Additional profiles hinting the roller-hinges
2 rollers-hinges (half)

## Slide 17
Fabrication & Installation
45 degrees frame cutting
Frame adjusting -2 / +5mm only with screws
Sophisticated caps, various gaskets, adjoining profile

## Slide 18
Fabrication & Installation
Roller hinges adjusting (4mm)
Shoot bolt adjusting (4,5mm)

## Slide 19
Fabrication & Installation
In case of even typologies
Additional profiles for integrating roller hinges
Special gaskets, caps
Roller hinges adjusting (4mm)

## Slide 20
Locking points
Special 5-point lock
3-point lock with hooks
plus additional shooting bolts (top/bottom)
better sealing and easy locking only through the handle

## Slide 21
Intermediate vents Locking points
ALUMIL design handle & handle locking
Quadruple (or double) shooting bolts

## Slide 22
“start from the correct glazing setting & bonding”
Basic Sections
It is recommended to bond all sash corners after vent squaring
24-44mm glazing thickness

## Slide 23
Max Dimensions – Wind load
without alum. reinforcement
Example
For vent width 1.0m, maximum height is
600Pa H = 2.5 m
800Pa H = 2.3 m
1200Pa H = 2.0 m
Up to 1.2m vent width
With 20mm (worst case), it does not exceed weight limitations

## Slide 24
Max Dimensions – Wind load
with alum. reinforcement
Example
For vent width 1.2m
with 20mm glass, up to 2.3m
with 18mm glass, up to 2.5m
with 16mm glass, up to 2.7m
Up to 1.3m vent width
Weight constraints is incorporated in the table

## Slide 25
Air permeability EN12207:2016-12
CLASS 3
Watertightness EN 12208:1999-11
Resistance to windload EN 12210:2016-03
Thermal insulation EN 10077-2
CLASS 8A
CLASS C2/B2
Uf from 2.2 W/m2K
Certifications (MF65)

## Slide 26
Certifications (MF65)
Thermal Insulation
 | Ug = 1,1 | Ug = 0,8 | Ug = 0,6
Uw | 1,54 | 1,29 | 1,13
For a 3+0 typology 2,6m x 2,8m (W x H) |  |  | 

## Slide 27
Commercial Section

## Slide 28
1. Minimal design & top aesthetics
  88 mm sash/sash face width
  100 mm frame/sash face width
Benefits

## Slide 29
2. Robustness and max dimensions
  Vents up to 1.3m width or 3.0m height
  Max dimension, e.g. 1.2 x 2.6m (with reinforcement)
  140 Kg per vent
Benefits

## Slide 30
Benefits
3. Range of solutions
insulated and non-insulted system
odd & even numbered typologies (n+0, n+1, n+m) & corner
standard or “balcony” door, opening inwards & outwards
double and triple glazing, standard & low threshold

## Slide 31
4. Easy fabrication & installation
thanks to
one single rail profile perimetrically (45° cutting)
no special machining (SMARTIA punching)
pre-drilled profiles & very simple vertical frame adjusting (with screws)
adjustable top/bottom roller-hinges
adjustable quadruple shoot bolts
Benefits

## Slide 32
5. Excellent performance & energy efficiency
  Water sealing 8A / 450 Pa (without sub sill)
  Thermal insulation Uw up to 1.11 W/m2K
  Air permeability CLASS 3
Benefits

## Slide 33
6. Long-lasting smooth operation
  High-quality, heavy-duty roller hinges set
  No problem even at the open position
140 Kg/vent
Benefits

## Slide 34
7. Enhanced burglar protection
  Quadruple shoot bolts
  5-point door locking
  Anti-lift mechanism
  Profile robustness
Benefits

## Slide 35
Benefits
Homeowners
Let natural light flood the space, and maximize outwards visibility (88mm sightline, 1.3m vent width)
Increase energy efficiency and cost savings thanks to the high thermal insulation
Enhanced burglar protection thanks to the quadruple bolts, the 3-point door locking, the anti-lift mechanism, etc.
Smooth operation and long-lasting flawless functionality

## Slide 36
Benefits
Architects
Minimal aesthetics and the lowest sightline (88mm).
Allow the design of high-performance buildings with energy efficient & money saving system.
Enhanced levels of burglar protection.
Very large & robust constructions, up to 1.3m width or 3m height.
Wide variety of solutions & typologies.
Smooth operation flawless in time.

## Slide 37
Benefits
Fabricators
Easy fabrication with one single rail profile placed perimetrically, 45° cutting and no need for special machining.
Easy installation thanks to adjustable roller-hinges & shooting bolts, pre-drilled profiles, very simple frame adjusting.
Bottom slide operation, thus no particular steel construction is needed which might be the case in top-hung.
Easy cost and offer estimation (profile pricing €/m).
Opportunity to increase clientele and personal prestige with this “value for money” product, ideal for commercial & residential use.

## Slide 38
Thank you for your attention